## Slide 1: Project #3 Pipelined MIPS Due data: May 22th
Seehwan Yoo
MSE.CIS.DKU
2018 spring

## Slide 2: Analogy with previous project
Make MIPS CPU emulator
Execute MIPS instructions (except for floating point ops)
  All of the front page instructions in Green sheet
Assume that you have memory, and program is loaded in memory before execution
Take MIPS binary program
  You can generate it with mips-gcc
Display the architectural state changes at every clock cycle
Handle exception gracefully

## Slide 3: Introduction to pipeline
Execution is performed through multiple stages
  IF (instruction fetch)
  ID (instruction decode)
  EXE (instruction execution)
  MEM (memory access)
  WB (write back result)
We assume each stage takes one cycle
  i.e. 5 cycles per instruction execution
We overlap execution of multiple instructions
  Ideally 5 instructions run at the same time
    Max. 5 in-flight instructions in pipeline

## Slide 4: Simulate pipeline in software
Cycle is updated at the end of instruction execution loop
  Until the cycle is changed, all hw operations are assumed to be executed in the same cycle
There are multiple in-flight instructions
  Use latch to hand over the stages
  Strictly depend upon the previous stage’s result latch
  Produce output on output latch
    Do NOT access global things
  Use input on input latch
At the end of cycle, latch handover is made
  Output latch values flow into input latch (in the next stage)

## Slide 5: An example) IF->ID (cont’)
Basic knowledge
  IF stage: read memory in which PC points to
  ID stage: decode instruction, and read register values
At the beginning:
  IF reads memory, and put the read value (instruction) on IF/ID latch
At the same time:
  ID gets the instruction from IF/ID latch,
  Decode instruction (opcode, rs, rt, rd, control signals),
  Read registers for rs, rt (if necessary),
  Perform sign-extension for imm,
  and put the produced value on ID/EX latch
    Read register values, sign-ext-imm, etc.

## Slide 6: An example) IF->ID
At the same time:
  ID gets the instruction from IF/ID latch,
  Decode instruction (opcode, rs, rt, rd, control signals),
  Read registers for rs, rt (if necessary),
  Perform sign-extension for imm
  and put the produced value on ID/EX latch
    Read register values, sign-ext-imm, etc.
At the end of cycle:
  IF/ID latch is filled by IF
  ID/EX latch is filled by ID

## Slide 7: Wrong way!
Note that multiple instructions are in-flight
  IF instruction, ID, EX, MEM, WB has all different instructions
Bad way to go
  Inside execution loop,
  IF produces result on IF/ID latch
  ID should take input from IF/ID latch
while (1) {
if_latch = fetch_inst();
ex_latch = decode_inst(if_latch);
// if_latch has overwritten by fetch_inst()!
…
}

## Slide 8: Another way (use input/output latches)
ID runs with input latch
  Which holds instruction
EX runs with input latch
  Which holds decoded instruction and read register values
…
ID produces result on output latch
  Which holds decoded instruction and read register values
EX produces result on output latch
  Which holds on ALU calculation result, memory address
At the end of cycle,
  Move output latch values  next stage input latch

## Slide 9: Data Dependency handling
Pipeline with data dependency
  Detect and wait
  Detect and forward/bypass
  Detect and eliminate
  Predict and verify
  Do something else
My suggestion (or additional implementation)
  Stalling
  Forwarding
  Scoreboarding

## Slide 10: Control dependency handling
Pipeline with control dependency
  Stalling
  Branch prediction
  Branch delay slot
  Fine-grained multi-threading
  Predicated execution
  Multipath execution
My suggestion (or additional implementation)
  Stalling
  Branch delay slot
  Branch prediction

## Slide 11: NOTE:
This program assignment is critical in your evaluation, so please work hard to complete in your schedule. If you need help, please ask for the help. (I am here for that specific purpose) I, of course, welcome any questions on the subject.
We will have demo time for some of your work (good/bad). In demo, you are asked to explain your software (structure/implementation). If you can, please think about the visualization of the emulator.
Note for the one strict rule that do not copy code from any others. Deep discussion on the subject is okay (and encouraged), but same code (or semantics) will result in sad ending.

## Slide 12: Requirements
The Objective: compare performance of pipelined vs. single-cycle u-processor.
  Your program should produce correct output. (and execution should be the same with code semantics)
  Compare the number of CPU clock cycles for single-cycle execution and pipelined execution. The clock cycles should be reasonably increased.
  In theory, we can reduce CPU clock cycle time by 1/5 in 5-stage pipelined execution.

## Slide 13: Machine Initialization
Before the execution, the binary file is loaded into the memory. Note that memory can be a data structure defined with large array.
Read all the file content into your memory (data structure).
Assume that initial RA value is 0xFFFF:FFFF.
  Thus, when your PC becomes 0xFFFF:FFFF, your machine completes execution, and halts.
Your application is loaded to 0x0, and initial stack pointer is 0x100000.
Rest of registers are initialized with value zero.

## Slide 14: Implementation requirements:
You should implement five-stage pipelined MIPS processor emulator. The emulator should implement IF, ID, EX, MEM, WB stages.
  For each stage, instruction execution has to be latched. That is, you have to store the execution state for each stages. Latches are the temporal storage that remember the execution states for each stages execution.
You can have separated instruction memory and data memory.
The emulated processor runs with the emulated clock cycle.
  You need to generate clock, which is a variable. The clock cycle increases only after all the work done in the all the stages. Note that max. 5 different instructions can run at the same cpu clock cycle.
You need to resolve data dependency among instructions. That is, you have to implement either stall, forwarding or register renaming. Forwarding is recommended as a basic implementation, but you can optionally choose to implement stall. You should make sure that it works, as in the program order (semantics).
You need to resolve control dependency among instructions. According to the MIPS ISA, one delayed branch slot is defined. Invalidation is basic implementation, but you can optionally implement branch prediction mechanisms.

## Slide 15: Output
Output: At the end of each cycle, the simulator prints out
  the changed micro-architectural state from the previous state.
  Micro-architectural state consists of set of general register, PC, and memory, and latches, internal data structure.
  You can print out only changed state.
After the execution completion, the simulator prints out
      Final result (r2)
      The total number of execution cycles
      Instructions execution statistics
        Total # instructions
        # of memory ops
        # of reg. ops
        # of (conditional) branches
        # of not-taken branches
        # of jumps
Think about good presentation of pipelined execution.
You can give log option in build time (e.g. #define DEBUG_IF)

## Slide 16: Evaluation:
Different credits are given for implementations, and demos.
More credits are allotted for different (hardware-based) hazard resolving techniques such as branch prediction, forwarding, stalling, etc.

## Slide 17: Input program binary:
You can use your own MIPS code (compiled) or download binary.
To make MIPS binary, use MIPS cross compiler toolchain.
  First, write C code, and compile mips-linux-gnu-gcc with “-c -mips1” option (compile only).
  Second, translate the object binary, stripping ELF headers. mips-linux-gnu-objcopy –O binary –j .text input.o input.bin.
  Third, check the integrity between binary files: objectdump, mips-linux-gnu-objdump –d input.o , vi –b input.bin  check with :%!xxd option. (google internet) or hexedit tool
To use with multiple functions, you need to hand-carve binary for function calls (jal 0, originally). For example, jal to 0x40 can be encoded as (0x0C000010).
Sample input file examples can be downloaded from the e-learning site. Two representative example programs are
  1) summation from 1 to 10,
  2) return 10,
  3) calculating 4 fibonacci,
  4)101-th smallest number from 10,000 random numbers
Some additional good examples are capturing N-way of counting coins, hanoii towers movements. Students who took system programming course can try them to implement in C/C++ language.

## Slide 18: Some advices
Advice one: You may need some time to think about your software structure, and operation, and pipeline. Therefore, think with note and pen, before rushing the code work.
Advice two: Make basic structure robust, and reliable. If you make code on suspicious base, you are easy to lose the way. Make print logs, before you have gone too much. Make basic structure, at the first hand. Make some checkpoints before you got failure.

## Slide 19: Strategic movements
Advice three: You can make things work from small pieces to a larger one. You may consider writing code in the following sequences.
  Make sure you have sound single cycle implementation
  Establish pipeline structure
  Make debug function
  Make basic control flow work (sequential execution path)
  Make reg. memory access instructions work
  Make pipeline with forwarding
  Make jump/branch work
  Make branch prediction

## Slide 20: Lastly,
Last advice, but not least: Begin as early as possible. Ask for help as early as possible. Try as early as possible. They are for your health-care.
Good Luck!